## Slide 1: CS 149: Operating Systems April 16 Class Meeting
Department of Computer Science San Jose State University Spring 2015 Instructor: Ron Mak
www.cs.sjsu.edu/~mak

## Slide 2: Polling
Producer-consumer relationship.
The OS and the device controller share a handshaking protocol.
The controller sets a busy bit in its status register to indicate that it’s busy working.
The OS sets a command-ready bit in the controller’s command register to indicate that it has a command for the controller to execute.

## Slide 3: The Polling Cycle
The OS repeatedly checks the busy bit.
  Polling (busy waiting)
The OS sets the write bit in the command register and writes a byte into the data-out register.
The OS sets the command-ready bit.
The controller sees the command-ready bit is set and sets the busy bit.

## Slide 4: The Polling Cycle, cont’d
The controller sees the write bit is set in the command register, reads the byte in the data-out register, and performs the I/O operation.
The controller clears the command-ready bit, clears the error bit in the status register, clears the write bit, and clears the busy bit.

## Slide 5: I/O Interrupts
An I/O device triggers the CPU’s interrupt-request line.
  An interrupt handler receives interrupts.
  Some interrupts can are maskable to ignore or delay the interrupts.
  Other interrupts are nonmaskable.
An interrupt vector dispatches the interrupt to the correct interrupt handler.
  Based on priority.

## Slide 6: OS-Level Interrupt Handlers
Interrupt priority levels
  A high-priority interrupt can preempt a low-priority interrupt.
Used to handle system exceptions (errors).
  Examples
    divide by zero
    accessing a protected or nonexistent memory address
    executing a privileged instruction in user mode

## Slide 7: Intel Pentium Processor Event Vector Table

## Slide 8: Application-Level Interrupt Handlers
Software interrupt (AKA trap)
A special instruction executed by a system call from a user application to request a kernel service.
User programs can include application-level interrupt handlers.

## Slide 9: Application-Level Interrupt Handlers
void INThandler(int);
main()
{
signal(SIGINT, INThandler);
printf("Sleep #1\n");
sleep(1);
printf("Sleep #2\n");
sleep(1);
printf("Sleep #3\n");
sleep(1);
...
}
interrupt2.c

## Slide 10: Application-Level Interrupt Handlers, cont’d
void INThandler(int);
...
void INThandler(int sig)
{
signal(sig, SIG_IGN);
printf("\nDo you really want to quit? [y/n] ");
int c = getchar();
if (c == 'y' || c == 'Y') {
exit(0);
}
else {
signal(SIGINT, INThandler);
getchar();
}
}
Demo
interrupt2.c

## Slide 11: Clocks and Timers
Provide current time and elapsed time.
Programmable interval timer
  Provide a timer to trigger operation X at time T.
  Used for timings
  Generate periodic interrupts
The UNIX ioctl() system call
  Covers odd aspects of I/O such as clocks and timers.

## Slide 12: Timer Example
#include <stdio.h>
#include <stdlib.h>
#include <assert.h>
#include <signal.h>
#include <sys/time.h>
int timedout = 0;
// The SIGALRM interrupt handler.
void SIGALRM_handler(int signo)
{
assert(signo == SIGALRM);
printf("\nTime's up!\nPress return for another.\n");
timedout = 1;
}
timers.c

## Slide 13: Timer Example
int main(void)
{
struct itimerval tval;
char string[BUFSIZ];
timerclear(& tval.it_interval);
timerclear(& tval.it_value);
tval.it_value.tv_sec = 3; // 3 second timeout
(void) signal(SIGALRM, SIGALRM_handler);
timers.c

## Slide 14: Timer Example, cont’d
for (;;) {
int i = rand()%10;
int j = rand()%10;
printf("Solve %d+%d=", i, j);
timedout = 0;
setitimer(ITIMER_REAL, &tval, NULL);
if (fgets(string, sizeof string, stdin) != NULL) {
if (!timedout) {
(void) setitimer(ITIMER_REAL, NULL, NULL);
printf(atoi(string) == i+j ? "Correct!\n" : "Wrong!\n");
}
}
else {
printf("\nGiving up?\n");
exit(0);
}
}
}
Generate and display a math problem.
Set the timer.
Turn off the timer.
timers.c

## Slide 15: The select() System Call
Manage a set of file descriptors.
Returns information about the file descriptors.
  Which have data waiting to be read.
  Which can accept data to be written.
Eliminates the need for polling.

## Slide 16: The select() System Call, cont’d
Return the number of ready file descriptors, 0 on timeout, or -1 on error.
Block while waiting for at least one file descriptor to become ready or until timeout.
#include <sys/time.h>
#include <sys/select.h>
int select(int nfds, fd_set *readfds, fd_set *writefds,
fd_set *exceptfds, struct timeval *timeout);

## Slide 17: The select() System Call, cont’d
Macros FD_ZERO(), FD_SET(), and FD_CLEAR() manipulate file descriptor sets.
Macro FD_ISSET() tests whether a file descriptor is in a set.

## Slide 18: Select Example
#include <stdio.h>
#include <stdlib.h>
#include <fcntl.h>
#include <unistd.h>
#include <sys/types.h>
#include <sys/time.h>
#include <sys/ioctl.h>
int main()
{
char buffer[128];
int result, nread;
fd_set inputs, inputfds; // sets of file descriptors
struct timeval timeout;
FD_ZERO(&inputs); // initialize inputs to the empty set
FD_SET(0, &inputs); // set file descriptor 0 (stdin)
...
}
select.c

## Slide 19: select() Example, cont’d
for (;;) {
inputfds = inputs; // restore input fd set
timeout.tv_sec = 2;
timeout.tv_usec = 500000;
result = select(FD_SETSIZE, &inputfds,
(fd_set *) 0, (fd_set *) 0, &timeout);
switch(result) {
case 0: {
printf("@");
fflush(stdout);
break;
}
case -1: {
perror("select");
exit(1);
}
No input.
Error
Wait for input on stdin for
a maximum of 2.5 seconds.

## Slide 20: select() Example, cont’d
default: {
if (FD_ISSET(0, &inputfds)) {
ioctl(0, FIONREAD, &nread);
if (nread == 0) {
printf("Keyboard input done.\n");
exit(0);
}
nread = read(0, buffer, nread);
buffer[nread] = 0;
printf("Read %d characters from the keyboard: %s",
nread, buffer);
}
break;
}
}
}
}
Got input! How many bytes
are available to read?
Demo

## Slide 21: Sockets
Network socket interface.
An application creates a software socket.
Connects a local socket to a remote address.
  The socket plugs the application into a socket created by another application.
Listen for data packets over the connection.

## Slide 22: Socket Example
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include <sys/types.h>
#include <sys/socket.h>
#include <sys/un.h>
#include "socket_name.h"
int main()
{
int server_sockfd, client_sockfd;
int server_len, client_len;
struct sockaddr_un server_address;
struct sockaddr_un client_address;
unlink(SOCKET_NAME);
server_sockfd = socket(AF_UNIX, SOCK_STREAM, 0);
...
}
server.c
Remove any old socket
and create an unnamed socket
for the server.

## Slide 23: Socket Example, cont’d
main()
{
...
server_address.sun_family = AF_UNIX;
strcpy(server_address.sun_path, SOCKET_NAME);
server_len = sizeof(server_address);
bind(server_sockfd, (struct sockaddr *)&server_address, server_len);
listen(server_sockfd, 5);
for (;;) {
printf("Server waiting.\n");
client_len = sizeof(client_address);
client_sockfd = accept(server_sockfd,
(struct sockaddr *) &client_address,
(socklen_t *) &client_len);
...
}
}
#define SOCKET_NAME "CS149_socket"
server.c
socket_name.h
Name the socket.
Create a connection queue
and wait for clients.
Accept a socket connection.

## Slide 24: Socket Example, cont’d
main()
{
...
for (;;) {
...
char ch;
read(client_sockfd, &ch, 1);
printf("Read character '%c'\n", ch);
ch++;
printf("Writing character '%c'\n", ch);
write(client_sockfd, &ch, 1);
// Close the socket.
close(client_sockfd);
}
}
server.c
Read a character from the socket.
Increment the character
and write it back to the socket.

## Slide 25: Socket Example, cont’d
#include <stdio.h>
#include <unistd.h>
#include <stdlib.h>
#include <sys/types.h>
#include <sys/socket.h>
#include <sys/un.h>
#include "socket_name.h"
int main()
{
int client_sockfd, len, result;
struct sockaddr_un address;
char ch = 'A';
client_sockfd = socket(AF_UNIX, SOCK_STREAM, 0);
address.sun_family = AF_UNIX;
strcpy(address.sun_path, SOCKET_NAME);
len = sizeof(address);
...
}
client.c
Create a socket for the client.
Name the socket.

## Slide 26: Socket Example, cont’d
main()
{
...
result = connect(client_sockfd, (struct sockaddr *)&address, len);
if (result == -1) {
perror("Error: client");
exit(1);
}
printf("Writing '%c' to the socket.\n", 'A');
write(client_sockfd, &ch, 1);
read(client_sockfd, &ch, 1);
printf("Read '%c' from the server.\n", ch);
close(client_sockfd);
exit(0);
}
client.c
Demo
Connect our socket to the server's socket.
Write 'A' to the
socket via sockfd.
Read what the
server sent back.

## Slide 27: How Fast?
Speed of an electrical signal: ~20 cm/nsec in a copper wire or optical fiber.
Heat dissipation
  Faster clock  more heat
  Smaller component  harder to dissipate heat
Clock speed | Max distance per cycle
10 GHz | 2 cm
100 GHz | 2 mm
1 THz | 100 microns

## Slide 28: Multiprocessor Systems
Physical limits to how fast and how small it is possible to make the CPU.
Solution: Computers with multiple CPUs.
  Massively parallel computers
Shared memory
Message-passing
Distributed
Modern Operating Systems, 3rd ed.
Andrew Tanenbaum
(c) 2008 Prentice-Hall, Inc.. 0-13-600663-9
All rights reserved

## Slide 29: Multiprocessor Operating Systems
Each CPU has its own operating system.
  Memory is partitioned.
Modern Operating Systems, 3rd ed.
Andrew Tanenbaum
(c) 2008 Prentice-Hall, Inc.. 0-13-600663-9
All rights reserved

## Slide 30: Multiprocessor Operating Systems, cont’d
Master-slave multiprocessors
  One copy of the OS runs on the master CPU.
  Slave CPUs redirect system calls to the master CPU.
Modern Operating Systems, 3rd ed.
Andrew Tanenbaum
(c) 2008 Prentice-Hall, Inc.. 0-13-600663-9
All rights reserved

## Slide 31: Multiprocessor Operating Systems, cont’d
Symmetric multiprocessor (SMP)
  One copy of the OS.
  Any CPU can run the OS.
  First acquire a mutex lock.
Modern Operating Systems, 3rd ed.
Andrew Tanenbaum
(c) 2008 Prentice-Hall, Inc.. 0-13-600663-9
All rights reserved

## Slide 32: Remote Procedure Call (RPC)
Client calls stub.
Stub packages (marshals) data into a message.
Kernel sends message to the server CPU.
Server stub receives message and unmarshals data.
Server stub calls the server procedure.
Modern Operating Systems, 3rd ed.
Andrew Tanenbaum
(c) 2008 Prentice-Hall, Inc.. 0-13-600663-9
All rights reserved

## Slide 33: Distributed Shared Memory (DSM)
Hardware
Operating system
User-level
Modern Operating Systems, 3rd ed.
Andrew Tanenbaum
(c) 2008 Prentice-Hall, Inc.. 0-13-600663-9
All rights reserved

## Slide 34: Distributed Shared Memory (DSM), cont’d
Pages of the address space are distributed among four CPUs. Page 10 is mapped to CPU 1.
CPU 0 references Page 10. It must wait for CPU 1 to release the page.
If Page 10 is read-only, it can be mapped to both CPU 0 and CPU 1.
Modern Operating Systems, 3rd ed.
Andrew Tanenbaum
(c) 2008 Prentice-Hall, Inc.. 0-13-600663-9
All rights reserved