## Slide 1: CS 149: Operating Systems April 23 Class Meeting
Department of Computer Science San Jose State University Spring 2015 Instructor: Ron Mak
www.cs.sjsu.edu/~mak

## Slide 2: Network Structure
Local area network (LAN)
  Network nodes are distributed over a small area
    one building
    adjacent buildings
Wide area network (WAN)
  Network node distributed over a large area
    entire country
    internationally _

## Slide 3: Local Area Network (LAN)
Covers a small geographical area.
  Bus, ring, or star network.
Speeds
  1 megabit/second: AppleTalk, infrared, Bluetooth
  10 megabits/second: 10BaseT Ethernet
  100 megabits/second: 100BaseT Ethernet

## Slide 4: Local Area Network (LAN), cont’d
Broadcast is fast and cheap.
  Including wifi.
Nodes:
  Usually workstations and/or personal computers
  A few (usually one or two) mainframes
  Gateway: a node that connects to other networks

## Slide 5: Local Area Network (LAN)
Operating Systems Concepts, 9th edition
Silberschatz, Galvin, and Gagne
(c) 2013 John Wiley & Sons. All rights reserved. 978-1-118-06333-0

## Slide 6: Wide Area Network (WAN)
Links geographically separated sites.
Point-to-point connections over long-haul lines.
  Often leased from a phone company.
  Communication processors control communication links.

## Slide 7: Wide Area Network (WAN)
Speeds
  1.544 megabits/second: T1 service
  45 megabits/second: T3 service
  40 gigabits/second: intercity backbone connections
Broadcast usually requires multiple messages.
Nodes:
  Usually a high percentage of mainframes.

## Slide 8: Wide Area Network (WAN)
Operating Systems Concepts, 9th edition
Silberschatz, Galvin, and Gagne
(c) 2013 John Wiley & Sons. All rights reserved. 978-1-118-06333-0

## Slide 9: Communication Structure
Naming and name resolution
  How do two processes locate each other to communicate?
Routing strategies
  How are messages sent through the network?
Connection strategies
  How do two processes send a sequence of messages? _

## Slide 10: Communication Structure, cont’d
Contention
  The network is a shared resource.
  How do we resolve conflicting demands for its use?

## Slide 11: Naming and Name Resolution
Systems on the network need to be named.
  Locally, each process has an id.
  A host on the network has no knowledge about processes on other hosts.
Identify processes on remote systems by a <host-name, identifier> pair.

## Slide 12: Domain Name Service (DNS)
Specifies the naming structure of the hosts.
Name to address resolution on the Internet.
  Hosts on the Internet are logically addressed with multipart names known as an IP (Internet protocol) address.
    Example: 172.7.57.62
  Maps domain names such as sjsu.edu to their IP addresses.

## Slide 13: Routing Strategies
How does a process at Site A communicate with a process at Site B?
How is the message routed?

## Slide 14: Fixed Routing
A path from A to B is specified in advance.
  The path changes only if a hardware failure disables it.
Since the shortest path is usually chosen, communication costs are minimized.
Fixed routing cannot adapt to load changes.
Ensures that messages will be delivered in the order in which they were sent.

## Slide 15: Virtual Routing
A path from A to B is fixed for the duration of one session.
Different sessions involving messages from A to B may have different paths.
Partial remedy to adapting to load changes.
Ensures that messages will be delivered in the order in which they were sent.

## Slide 16: Dynamic Routing
The path used to send a message from site A to site B is chosen only when a message is sent.
Usually a site sends a message to another site on the link least used at that particular time.
Adapts to load changes by avoiding routing messages on heavily used paths.

## Slide 17: Dynamic Routing
Messages may arrive out of order.
How to remedy this problem?
  Append a sequence number to each message.

## Slide 18: Connection Strategies
Once routing has been established, messages can reach their destinations.
Processes at different sites that want to communicate with each other must choose a connection strategy.

## Slide 19: Connection Strategies, cont’d
Circuit switching
  A permanent physical link is established for the duration of the communication.
  Example: telephone system
Message switching
  A temporary link is established for the duration of one message transfer.
  Example: post-office mailing system

## Slide 20: Connection Strategies, cont’d
Packet switching
  Messages of variable length are divided into fixed-length packets which are sent to the destination.
  Each packet may take a different path through the network.
  The packets must be reassembled into messages as they arrive.

## Slide 21: Connection Strategies, cont’d
Circuit switching requires setup time, but incurs less overhead for shipping each message, and may waste network bandwidth.
Message and packet switching require less setup time, but incur more overhead per message.

## Slide 22: Contention
Several sites may want to transmit information over a link simultaneously, causing collisions.
CSMA/CD
  Carrier sense with multiple access (CSMA)
  Collision detection (CD)
  A site determines whether another message is currently being transmitted over that link.
  If two or more sites begin transmitting at exactly the same time, they register a CD and will stop transmitting.

## Slide 23: Contention, cont’d
CSMA/CD, cont’d
  When the system is very busy, many collisions may occur.
    Performance may be degraded.
  CSMA/CD is used successfully in the Ethernet system, the most common network system.

## Slide 24: Communications Protocols
The ISO (International Standards Organization) 7-layer model.
Layer 1: Physical layer
  Handle the mechanical and electrical details of the physical transmission of a bit stream.
Layer 2: Data-link layer
  Handle the frames, or fixed-length parts of packets.
  Error detection and recovery that occurred in the physical layer.

## Slide 25: The ISO Network Model
Layer 3: Network layer
  Connect and route packets in the communication network.
  Handle the address of outgoing packets.
  Decode the address of incoming packets.
  Maintain routing information for proper response to changing load levels.
  Routers work at this level.

## Slide 26: The ISO Network Model
Layer 4: Transport layer
  Low-level network access and for message transfer between clients.
  Partition messages into packets.
  Maintain packet order.
  Control flow.
  Generate physical addresses.

## Slide 27: The ISO Network Model
Layer 5: Session layer
  Implement sessions, or process-to-process communications protocols.
Layer 6: Presentation layer
  Resolve the differences in formats among the various sites in the network
    Character conversions
    Half duplex/full duplex (echoing)

## Slide 28: The ISO Network Model
Layer 7: Application layer
  Interact directly with the users
  File transfer
  Remote-login protocols
  Electronic mail
  Schemas for distributed databases

## Slide 29: The ISO Network Model
Operating Systems Concepts, 9th edition
Silberschatz, Galvin, and Gagne
(c) 2013 John Wiley & Sons. All rights reserved. 978-1-118-06333-0

## Slide 30: The ISO Network Model
Operating Systems Concepts, 9th edition
Silberschatz, Galvin, and Gagne
(c) 2013 John Wiley & Sons. All rights reserved. 978-1-118-06333-0

## Slide 31: TCP/IP Protocol Layers
Operating Systems Concepts, 9th edition
Silberschatz, Galvin, and Gagne
(c) 2013 John Wiley & Sons. All rights reserved. 978-1-118-06333-0

## Slide 32: Ethernet Packet Transmission
Every host has a unique IP address.
  Host: a computer connected to the network.
  The Domain Name Service (DNS) can be used to acquire IP addresses.
Every Ethernet device has a unique medium access control (MAC) address.
  Two devices on a LAN communicate using only their MAC addresses.

## Slide 33: Ethernet Packet Transmission, cont’d
Address Resolution Protocol (ARP) is used to send data to another system.
If the hosts are on the same network, ARP can be used.
If the hosts are on different networks, the sending host will send the packet to a router, a device which routes the packet to the destination network.

## Slide 34: An Ethernet Packet
Operating Systems Concepts, 9th edition
Silberschatz, Galvin, and Gagne
(c) 2013 John Wiley & Sons. All rights reserved. 978-1-118-06333-0

## Slide 35: Failure Detection
Detecting hardware failure is difficult.
Use a handshaking protocol to detect link failure.
Assume Site A and Site B have established a link.
At fixed intervals, sites exchange I-am-up messages to indicate that they are up and running.

## Slide 36: Failure Detection, cont’d
If Site A does not receive a message within the fixed interval, it assumes either
  The other site is not up, or
  The message was lost.
Site A sends an Are-you-up? message to Site B.
If Site A does not receive a reply, it can repeat the message or try an alternate route to Site B.

## Slide 37: Failure Detection, cont’d
If Site A does not ultimately receive a reply from Site B, it concludes some type of failure has occurred.
Types of failures:
  Site B is down
  The direct link between A and B is down
  The alternate link from A to B is down
  The message has been lost

## Slide 38: Failure Detection, cont’d
However, Site A cannot determine exactly why the failure has occurred.

## Slide 39: Reconfiguration
When Site A determines a failure has occurred, it must reconfigure the system.
If the link has failed from A to B, this must be broadcast to every site in the system.
If a site has failed, every other site must also be notified that the services offered by the failed site are no longer available.

## Slide 40: Reconfiguration, cont’d
When the link or the site becomes available again, this information must be broadcast to all other sites.

## Slide 41: Network Design Issues
Transparency
  The distributed system should appear as a conventional, centralized system to the user.
Fault tolerance
  The distributed system continues to function after a failure. _

## Slide 42: Network Design Issues
Scalability
  As demands increase, the system easily accepts the addition of new resources to accommodate the increased demand.
Clusters
  A collection of semi-autonomous machines acts as a single system.